## Slide 1
MASTER OF ELECTRICAL ENGINEERING FOR COMMUNICATIONS & INFORMATION PROCESSING
Radio Frequency for Connected Objects
Project: INDOOR POSITIONING WITH WiFi
By
Areeb Tariq
Muhammed Fatih Koc
Ahmed Waheed
Karthik Pandey
Date: 24 June 2021

## Slide 2
MASTER OF ELECTRICAL ENGINEERING FOR COMMUNICATIONS & INFORMATION PROCESSING
Radio Frequency for Connected Objects
Project: Positioning System Project With GPS-WiFi-INS Fusion
By
Areeb Tariq
Muhammed Fatih Koc
Ahmed Waheed
Karthik Pandey
Date: 24 June 2021

## Slide 3: Outline
Background and Introduction
Motivation
Model Space and Validity
Experiments, Parameters of the model, and Defined User states
Process flow and Activity Timeline
Challenges and Solutions
Implementation and Algorithm
Results Observations and Remarks
Limitations
Future Variations
Software Tools
Conclusion
DEMO

## Slide 4: Background/Introduction
Ubiquitous positioning technology
Fusion technology for seamless transition between varied environment
Proposed positioning system should be economical ,reliable and continuous.
We would propose to use the Sensor technology(GNSS-WLAN-INS) in our model in order to achieve seamless integrity and continuous (Quality of Service)in different user states; transitions etc..

## Slide 5: Motivation
Fusion technique
Sensors like magnetometer, accelerometer, gyroscope
Different environments positioning
Positioning accuracy ranges

## Slide 6: Validity and Model Space
Experiments conducted with the mobile device in horizontal plane
Valid in both indoor, outdoor, with transitions

## Slide 7: Experiments
1. Straight outdoor
2. L shape outdoor
3. Straight indoor
4. L shape indoor
5. Straight outdoor - straight indoor
6. L shape outdoor-indoor
7. Straight indoor-outdoor
8. L shape indoor-outdoor
9. Straight outdoor (150m longer distance)

## Slide 8: Implementation of Sensors (1)
Accelerometer
Step counter method.
Acceleration data is extracted through code.
Mean is scaled to obtain zero crossings
Calculated number of steps from number of zero crossings
Multiplied with step size = 0.6 m to find the distance
GPS
From latitude and longitude coordinates, found the distance in code

## Slide 9: Implementation of Sensors (2)
Magnetometer
Conducted repeated experiments to map magnetometer values to angular movement
Thresholds are defined in code
Gyrometer
The spikes were used to identify the direction of angular movement (clockwise or counterclockwise)

## Slide 10: Parameters of the model
TOTAL_READINGS (defines the maximum of readings for one sensor)
ACC_SAMPLING_FREQ , GPS_SAMPLING_FREQ , MAG_SAMPLING_FREQ , GYR_SAMPLING_FREQ
FOOTSTEP_SIZE (defines the step size value, by default 0.6m)
GPS_TIME_TRANSITION_MS (defines the range in ms to observe the next GPS recording)
GPS_ACC_TRANSITION_THRESHOLD (defines the threshold determining which sensor is preferred)
GYRO_LOWER_THRESHOLD (defines the threshold value for clockwise direction)
GYRO_UPPER_THRESHOLD (defines the threshold value for counter clockwise direction)
MAG_THRESHOLD (defines the threshold for magnetometer to handle noise)
WIFI_POWER_THRESHOLD (defines the threshold to indicate the power level in indoor)

## Slide 11: Defined User States
OUTDOOR
TRANSITION
INDOOR
INDOOR_NO_WIFI

## Slide 12: Process Flow
5 Sensors record measurments
File Processing to extract specific sensor
Distance Calculation through Accelerometer and GPS
Angular movement through Gyrometer and Magnetometer
Fusion Algorithm
Write results to file

## Slide 13: Activity Timeline
Experimentation and observation with INS
Analyzing INS sensitivity with movements
Designed outdoor, indoor, and transition space
Conducted experiments
Automated the processing and algorithm on software
Estimation and evaluation of results

## Slide 14: Challenges
Noise fluctuations in INS
Unavailability of continuous outdoor space with previous WiFi positioning space
Non-uniform sampling frequency of INS
Processing of the data

## Slide 15: Solutions
Noise fluctuations in INS
Applied averaging and inserted thresholds [IN DEMO]
Unavailability of continuous outdoor space with previous WiFi positioning space
Separated spaces (Outdoor+Transition, Indoor+Transition)
Non-uniform sampling frequency of INS
Added user controlled sampling feature in code [IN DEMO]
Processing of the data
Automated through code to process and extract data in C code [IN DEMO]

## Slide 16: Fusion Algorithm (1)
Takes the reference time from the first recording of accelerometer as t=0.
Checks if within threshold time (say 1.2s) there is a GPS recording.
If yes, calculate the distance based on that GPS recording
At the same time, calculate the distance from the accelerometer from initial time to this GPS reading time.
Compare these two distances with GPS_ACC threshold which defines which sensor is to be preferred.
If the difference is huge (depending upon threshold), ACC is preferred.
Otherwise (depending upon threshold) GPS is preferred.

## Slide 17: Fusion Algorithm (2)
If there is no GPS recording within maximum time jump, distance data is evaluated from the ACC sensor
Each distance recording is marked with the timestamp
In parallel, using gyrometer (high sensitivity), we determine the angular direction at any timestamp.
During this time, the angular movement is determined by the magnetometer.
Condition: If gyro indicates movement, consider magneto’s angular reading
Having distance and angle, find XY using geometry
Write XY automatically to Excel file and plot to observe the route

## Slide 18: Fusion Algorithm (3)
If WiFi with known MAC address is detected and power level is within the theshold, the fusion algorithm extracts the positioning information from the code of project 1
This is implemented in code, but difficult to experiment since we didn’t have the outdoor space near WiFi indoor positioning model.

## Slide 19: Results
Case where GPS is corrupted
Case where ACC has errors (long distance)
Experimental scenarios
[SHOWN IN DEMO]

## Slide 20: Observations and Comments
For every 15m, on average accelerometer step counter gives an error of 1m.
In longer distances, accelerometer gets more and more inaccurate with step counter
It is compensated by the GPS in outdoor but in indoor the WiFi positioning isn’t as accurate as GPS, so in indoor, longer distances are less reliable.
Magnetometer is very sensitive to relative motion of device with the body which needs to be modeled with detailed experiments and with different human beings
Gyrometer is highly sensitive and gives clear indication of angular direction even with slower speeds. This is helpful in fusion algorithm.

## Slide 21: Limitations
Current implementation is limited to horizontal placement of the mobile device
This model is not perfect in removing the noise from INS
It doesn’t model lot of humans data because of limited scope and time

## Slide 22: Future Recommendations
The noise can be filtered from the data
The magnetometer can be modeled more accurately
Can be extended for any position of mobile device

## Slide 23: Software Tools
Excel files (ACC, GYR, MAG, GPS, WIFI): Files containing the data extracted from the sensor
Excel file (XY DATA): File containing data of the estimated XY
C++ (Fusion_Project): User friendly software with input sensor log file and automatically implements extraction of data, fusion algorithm, and writing of data to excel files
All these files are provided with ReadMe files for user to assist in using these applications

## Slide 24: Conclusion
Introduced the Indoor WiFi positioning and Fusion Sensor projects
Discussed about the validity and limitations of both models
Explained the process flows and activity timelines for both models
Discussed Experimental procedure and components for both models
Listed key challenges and solutions for both models
Described the algorithm and proposed models
Shared the results and observations
Provided the future modifications for both models
Listed the software tools and solutions produced as part of project

## Slide 25: Thank you Questions?